## Slide 1: UNIT- 4 TRANSFORMER

## Slide 2: TRANSFORMER

## Slide 71: Application of Transformer
85
It can rise or lower the level of level of Voltage or Current
( when voltage increases, current decreases and vice-versa because P =V x I, and Power is same ) in an AC Circuit.
It can increase or decrease the value of capacitor, an inductor or resistance in an AC circuit. It can thus act as an impedance transferring device.
It can be used to prevent DC from passing from one circuit to the other.
it can isolate two circuits electrically.

## Slide 72: Three Phase Transformer

## Slide 76: Numerical: Three Phase Transformer

## Slide 84: Measuring Instruments
Classification 1
Absolute
Secondary
Indicating
Recording
Integrating
Classification 2
AC
DC
AC/DC
8
Current, voltage, power, etc. Not visible to eyes &
must be measured using meters.
Classification 1
  Absolute: Quantity is measured in terms of instrument constant and deflection
  Secondary: Calibrated using Absolute instrument. Give
measurement directly.
    Indicating: magnitude indicated directly
    Recording: continuous record of variations of magnitude over a definite period of time
    Integrating: total amount of electrical energy supplied over time
Classification 2
  DC: measure only DC quantities
  AC: measure only AC quantities
  AC/DC: measure both AC as well as DC quantities

## Slide 85: Measuring Instruments: Types of Torques
 Deflecting Torque: moves pointer from its
9
zero position during measurement
Controlling Torque
  Opposes deflecting torque
  Limits pointer movement to ensure correct
measurement
  Returns pointer to 0 under absence of deflecting torque
Controlling torque provided by
  Spring Control
 As pointer moves, Phosphor bronze hair spring gets twisting.This twist produces controlling torque
 Spring subjected to fatigue with time, temperature
coefficient of stiffness of spring affects measurement
Gravity Control
  Small weight attached to moving system to produce controlling torque
  Cheap, not subjected to fatigue, unaffected by change in temperature
  Must be kept vertical, non-uniform scale
Damping Torque
position
prevents oscillation of pointer about final deflecting
Brings pointer to rest
Damping torque provided by
  Air-friction damping
    Piston (connected to pointer) moves in fixed air chamber, building pressure inside that opposes further piston motion
  Fluid-friction damping
    Light vanes/disk attached to moving system move in damping oil
  Eddy-current damping
    Eddy currents set up when sheet of conducting (non-magnetic) material moves in magnetic field
    Eddy currents set up force to oppose this motion
    Cannot be used where introduction of permanent magnet for eddy currents will distort the existing magnetic field

## Slide 86: Moving Iron Instrument: Attraction type
Principle: Attraction of single piece of iron into magnetic field
Operation:
  Current to be measured passed through coil, setting up magnetic field
  Moving iron is magnetized and attracted to the coil, and pointer moves
Spring Control and Air-friction damping
Operating torque
  Low when moving iron just enters solenoid.
Hence, Scale cramped at lower end
  Increases rapidly as moving iron drawn in.
Hence, Scale expanded at upper end


10

## Slide 87: Moving Iron Instrument: Repulsion type
Principle: Repulsion of two adjacent iron pieces magnetized by same magnetic field
Operation:
  Current to be measured passed through coil, setting up magnetic field which magnetizes both irons in same direction
  Repulsive force set up
  Moving iron repelled by fixed iron, and
pointer moves
Spring Control and Air-friction damping
Non-uniform scale
AC and DC Measurements: deflecting
torque depends on I 2
11

## Slide 88: Moving Coil Instruments: Permanent Magnet
DC measurements only
At AC, pointer follows current direction and quivers
around zero mark
12
Td
Principle: Current carrying conductor, placed in magnetic field, experiences torque
Operation:
  Current to be measured passed through coil
  Coil experiences deflecting torque due to electromagnetic effect from magnetic field of magnet
  Controlling torque by 2 phosphor bronze
conducting springs
Spring Control and Eddy-current damping
 I and Tc . For steady deflection,
Moving Coil (PMMC)
Tc  Td
 I, i.e. Uniform Scale

## Slide 89: Moving Coil Instruments: Dynamometer-type

Td  if im
Moving Coil
and Tc . For steady deflection, Tc  Td
f m
 AC/DC measurements
 i i  i2, i.e. Non-uniform Scale
Principle: Current carrying conductor, placed in magnetic field, experiences torque
Operation:
  Current to be measured passed through Fixed air-cored coil
  Fixed Coil (divided in 2 parts) in series with Moving Coil
  Coils placed parallel to each other to allow movement of Moving Coil between 2 halves of Fixed coil
  Deflecting torque due to interaction of magnetic fields created by if in Fixed Coil and im Moving Coil
Spring Control and Air-friction damping

## Slide 90: Extension of Range
Increasing instrument range for measuring large currents, voltages or power
Commonly used: Ammeter Shunts &Voltage Multipliers
Ammeter Shunt
  A low resistance in parallel with coil circuit of instrument
  Greater part of circuit current passes through shunt
  Shunt has 2 types of terminals, viz. Current and Potential
Voltmeter Multiplier
  A high non-inductive resistance (Manganin) in series with instrument coil
  Allows measurement of high voltage

## Slide 91: Ammeter Shunt
, where
is the multiplying factor, and
Terminology
  Rm : Internal resistance of coil, Rsh : Shunt resistance
  Im : Full-scale deflection current, Ish : Shunt current
Voltages across shunt and coil are equal, i.e.

This gives,


## Slide 92: Voltmeter Multiplier
is the required series resistance
Terminology
  Rv :Voltmeter resistance, R : Series resistance
  Im : Full-scale deflection current

v
I•m
 We have, V  Im Rv
Im R
R  V  R

## Slide 93: Dynamometer-type Wattmeter
Wattmeter: Combination of ammeter (Current Coil) & voltmeter (Pressure Coil)
Current Coil is Fixed Coil (divided into 2 parts) & carries current to be measured
Pressure coil is Moving Coil, in parallel with supply, carries current proportional to supply voltage
Operation:
  Deflecting torque due to interaction of magnetic fields created by currents in Fixed and Moving Coils
  Pointer (Moving Coil) turns about its axis
 Uniform Scale
d f m
max
max
0
inst av
 T  i i  iv R  T  iv  T
2
 1
V sin I sin() d
2 
2 2
d
V I
 T  max max cos VI cos